## Slide 1: Bypassing obstacles on S.W. – algorithm modules
Run-time | Performance test | Output module | Output | Input | Input module | Module name
Matlab: Python: | Walk for 50m and set stride parameters K1&k2 such that the cumulative strides length is 50m | Scan matching | IMU X-Y translations at 6Hz | IMU acceleration raw data at 200Hz | RealSense, IMU, accelerometer, | Translation filter
 | Compare STD of P.C. in z-axis inside a bounding box around the center of the plane to a bounding frame surrounding this box | Scan matching | Rotated P.C. frame | P.C. ; euler angles (madgwick filter) | RealSense, P.C. Euler angles pitch and roll (IMU) | P.C. Plane fit
 | Compare translation based on IMU with translation based on scan matching, compare yaw angle to derived yaw angle, | SLAM | Frame (i to i+1) translation and yaw; d-frame top view, | Rotated P.C. frames (i-1 and i); frame (i-1 to i) translation; Yaw and texture; | 1. P.C. Plane fit 2. RealSense texture 3. IMU yaw 4. Translation filter | Scan matching
 | Measure the width along the 50m route on the S.W. and compare it to that derived from the SLAM | Control | SLAM | Translations and yaw, D-frames - top view, | Scan matching | SLAM
 |  | User feedback | Vibration control | SLAM | SLAM | Control
 |  | NA | Activating # motor 1/ 2/ 3 | Activating motor # 1/ 2/ 3 | Control | User feedback

## Slide 2
P.C. Plane fit
Euler angles pitch and roll (IMU)
R.S. P.C.
Translation filter
Scan matching
Motion direction
Euler angle yaw (IMU)
SLAM
Control
R.S. ax,ay,az
R.S. texture
User feedback
Bypassing obstacles on S.W. – algorithm modules